Rubric points:
-> The car is able to drive at least 4.32 miles without incident
Yes, The car is able to drive without any incidents for more than 4.32 miles

-> The car drives according to the speed limit
Yes, The car doesn’t exceed a maximum speed of 50 mph. To achieve this i used a reference speed variable. This variable is decreased whenever the speed reached 50mph, meanwhile increased when ther is no car ahead.
Code line : 385 to 392

-> Max Acceleration and Jerk are not Exceeded
Yes, the reference speed is either increased or decreased @ a rate of .225 mph per 0.02 sec. This corresponds to a maximum 5 m/s2
Code line : 385 to 392

-> Car does not have collisions
If any car is detected on the same lane in front of the ego vehicle. Then, the ego vehicle reduces it’s speed until the distance between the ego vehicles current position and future position of the detected vehicle is less than 40 m.

Code line : 337 to 340

-> The car stays in its lane, except for the time between changing lanes
The trajectory for the ego vehicle is generated using spline. The S & D values @ various time intervals in fernet cordinated are used to generate a smooth trajectory. In order to stay in a lane, the D value is always chosen in the middle of the lane. Eg: for the car to always stay in the middle lane, The D value is always chosen as 6

code line : 430 to 433

-> The car is able to change lanes
The lane change is done, whenever the vehicle infront of the ego vehicle drives slowly and the vehivles in the switching lane are far enough for a possible collision to avoid. The switching lane is decided based on the current lane.i.e if the ego vehicle is in lane 0, then it is allowed only to switch to lane 1.

Code line : 345 to 377